## Slide 1: SNU-Samsung AI (NPEX) Lab 1: Verilog 101 - Register File Design Junseo Lee (TA) Seoul National University

## Slide 2: Goal of Lab 1
The objective of Lab 1 is to design a register file
In this Lab, you will do
  Implement your register file
  Validate your register file with the provided testbench

## Slide 3: Outline
Background
  RISC processor
  Register file
Educational Materials
  Verilog 101
  Example code: 4:2 encoder
Register File Design
  Specification
  Pseudo code example
Result
  Behavioral simulation

## Slide 4
Background

## Slide 5: Background #1 : RISC processor
RISC (Reduced Instruction Set Computer)
  Computer design that reduces the number of CPU instructions in order to simplify the internal structure
Execution of the instruction can be classified into 2 stages
  Fetch stage: Reads the instruction from instruction memory
  Execute stage: Executes the right work based on the read instruction in the fetch stage

## Slide 6: Background #1 : RISC processor
Fetch Stage : Reads the instruction from instruction memory
  PC (Program counter)
    Register that holds the address of the next instruction (which is stored in instruction memory)
  Instruction Memory
    A part of memory that stores the instruction to be executed
  Instruction Register
    Register that stores the instruction which is fetched from instruction memory
1) Fetch instruction from instruction memory
2) Store fetched instruction in the instruction register

## Slide 7: Background #1 : RISC processor
Execute stage: Executes the instruction fetched in fetch stage
  Register file
    A group of registers that temporarily hold the data required by the instruction
  Decoder
    A combinational logic that determines the action to be executed by decoding opcode
  Data Memory
    A part of memory that stores the data
  ALU/Shifter
    A combinational logic that executes ALU / shifter operations depending on the decoder’s result
Store the data required by instruction in the register file
2) Decode the opcode of the instruction
3) Execute the operation depending on the
decoder’s result

## Slide 8: Background #2 : Register file
Register file temporarily stores data required by the instruction
  It stores operands, memory addresses, etc.
  It also passes data to the functional unit
Register file reads / writes data to the input address
Register file consists of multiple registers
  Each register has unique ID
Data 2
Data 1
Data 0
…
Data 15
r2
r1
r0
r15
…
Example of register file with 16 registers
n

## Slide 9: Background #2 : Register file
Input / Output of register file
  Input
    Addr_A , Addr_B : Input address
    WR : Signal to notify register file that data write is in progress. Generated by the decoder
    CLK : Clock Signal
    RSTn : Negative Reset Signal
    Data_in : Input data
  Output
    Src : Data stored in Addr_A
    Dest: Data stored in Addr_B
n

## Slide 10: Register file operation example
Behavior of register file with actual assembly instruction
  Read Operation
    Read r3 / r4 from register file, then pass to ALU
  Write Operation
    Write the result (r3+r4) to r4
Specification
  8 registers (each register is 16bit)
  Rising CLK edge triggered
ADD r4, r3, r4
r4 = r3 + r4
Addr_B
r7
r6
r5
r4
r3
r2
r1
r0
Addr_A
Data_in
Src
Dest
CLK
WR
RSTn

## Slide 11: Register file operation example
Read Operation
    Data in Addr_A register  Src
    Data in Addr_B register  Dest
    Combinational logic (not affected by CLK)
ALU
Addr_B
r7
b
a
r6
r5
r4
r3
r2
r1
r0
Addr_A
Data_in
Src
Dest
CLK
WR
RSTn
a + b
0011
0100

## Slide 12: Register file operation example
Write Operation
    Destination : Addr_B register
    Data: Data_in (from ALU adder in this example)
    Condition : Rising edge(posedge) CLK, Positive WR
    Sequential logic (affected by CLK)
Addr_B
r7
a + b
a
r6
r5
r4
r3
r2
r1
r0
Addr_A
Data_in
Src
Dest
CLK
WR
RSTn
a + b
ALU
0100

## Slide 13
Educational Materials

## Slide 14: Verilog 101
Number representation
  Format should be : <size>’<base format><number>
  Size : The size of the data with bit granularity
  Base format: radix
  Number : The value of the data
Assign statement
  You can assign the value to the data with assign statement
Vector & Array
assign a = 4’b0100; // 4bit binary, value: unsigned 4
assign a = 3’d100 // 3bit decimal, value: unsigned 100
assign a = 8’h0a // 8bit hexadecimal, value: unsigned 11
reg register_1; // 1bit reg
reg [7:0] register_2; // 8bit reg
reg [7:0] reg_array_1[15:0]; // 8bit x 16 array
reg_array_1[2] = register_2;

## Slide 15: Verilog 101
Always block
  Starts running from simulation time 0
  Executes whenever signal changes (indicated in sensitivity list) during simulation
Conditional / Loop statement
  You can use conditional / loop statement (e.g., for, if, case) inside the “always block”
always @(A, B) // executes when A or B changes
begin
…
end
always @(*) // execute when any signal changes
begin
…
end
always @(A, B)
begin
if(condition) begin
…
end
end
always @(A, B)
begin
for(condition) begin
…
end
end

## Slide 16: Verilog 101
Combinational logic design
  Continuous assignment : executes when right-value changes, regardless of the order in code
  ‘=‘ operator
    It indicates continuous assignment outside of the always block
    It indicates that code is executed sequentially within the always block
Sequential logic design
  ‘<=‘ operator
    It indicates that code is executed concurrently within the always block
// continuous assignment
wire a;
assign a = 2’b00;
always@*
begin
b = 2’b00;
c = 2’b01; // Assignment to b and c is executed sequentially
end
always@(posedge CLK)
begin
b <= 2’b00;
c <= 2’b01; // Assignment to b and c is executed concurrently
end

## Slide 17: Verilog 101 : 4:2 Encoder
We will be synthesizing a simple 4:2 encoder
4:2 Encoder
Y3
Y2
Y1
Y0
A0
A1
Input (Y3, Y2, Y1, Y0) | Output (A1, A0)
(1, 0, 0, 0) | 3 (1, 1)
(0, 1, 0, 0) | 2 (1, 0)
(0, 0, 1, 0) | 1 (0, 1)
(0, 0, 0, 1) | 0 (0,0)
Everything else | 0

## Slide 18: Verilog 101 : 4:2 Encoder
This is the Verilog code for the 4:2 encoder
/**
* encoder4to2.v: encoder4to2 module
*
* 4 to 2 encoder: (Y3, Y2, Y1, Y0) => (A1, A0)
*
* (1, 0, 0, 0) => 3
* (0, 1, 0, 0) => 2
* (0, 0, 1, 0) => 1
* (0, 0, 0, 1) => 0
* everything else => 0
*/
// note that the default port type is 'wire'
module encoder4to2(
input Y0,
input Y1,
input Y2,
input Y3,
output reg [1:0] A
);
// use @* for combinational logic always blocks
always @*
begin
if (Y0 == 1 && Y1 == 0 && Y2 == 0 && Y3 == 0) begin
A = 2'b00;
end
else if (Y0 == 0 && Y1 == 1 && Y2 == 0 && Y3 == 0) begin
A = 2'b01;
end
else if (Y0 == 0 && Y1 == 0 && Y2 == 1 && Y3 == 0) begin
A = 2'b10;
end
else if (Y0 == 0 && Y1 == 0 && Y2 == 0 && Y3 == 1) begin
A = 2'b11;
end
else A = 2'b00;
end
endmodule

## Slide 19
Lab 1: Design your register file

## Slide 20: Specification of register file
You need to design a register file with 8 registers
  Each register should be 16 bit
Below operations should be supported
  Read: Reads Addr_A / Addr_B register then outputs to Src/Dest
  Write : Writes Data_in to Addr_B register
  Reset : Resets all registers to 0x00 when RSTn is negative
Input / Output specification
  CLK, RSTn, WR (1 bit)
  Addr_A, Addr_B (4bit)
    However, you may use lower 3-bit since there are only 8 registers
  Data_in (16 bit)
  Src, Dest (16bit)
Addr_B
r7
r6
r5
r4
r3
r2
r1
r0
Addr_A
Data_in
Src
Dest
CLK
WR
RSTn

## Slide 21: Pseudo-code example
What you need to modify
  Type of module
  Name of module instance
  Name of ports

## Slide 22: Pseudo-code example
if (RSTn.negedge or CLK.posedge)
{
if (!RSTn)
reset all regs
else if (WR)
reg[ADDR_B] = DATA_IN
}
SRC = reg[ADDR_A]
DEST = reg[ADDR_B]
Reset/Write operation  Sequential Logic
Read operation  Combinational Logic
Register file operation pseudo-code

## Slide 23
Result

## Slide 24: Result
You can test your register file with provided testbench (register_file_tb.v)
  In the server, you can use iverilog for verilog simulation
  iverilog is already usable in the server, so just write command: make; ./register_file;
  If you download Vivado at local, you can also check the waveform from behavior simulation
Sample waveform

## Slide 25: Result
Verilog Simulation in Terminal