## Slide 1: SNU-Samsung AI (NPEX) Lab 2: Implementing FC with Verilog Joonho Hwangbo (TA) Seoul National University

## Slide 2
Background

## Slide 3: Reference
CS231n: Convolutional Neural Networks for Visual Recognition
Standford CS231n lecture note (translated)
  Neural network: http://aikorea.org/cs231n/neural-networks-1/
  Convolutional network: http://aikorea.org/cs231n/convolutional-networks/
CNN, Convolution Neural Network summary
  Personal Blog: http://bitly.kr/cb6DwW

## Slide 4: Background: CNN Network
FC (Fully-Connected) layer
Neural Network for Image Classification
source: https://adeshpande3.github.io/A-Beginner%27s-Guide-To-Understanding-Convolutional-Neural-Networks/

## Slide 5: Background: FC Layer
FC layer’s operation
Structure of FC layer 1)
Operation of FC layer2)
m
Weight
Input
Bias
=
Output
]
[
1) http://needjarvis.tistory.com/182
2) https://petewarden.com/2015/04/20/why-gemm-is-at-the-heart-of-deep-learning/

## Slide 6: FC: Example
8x4 FC layer
  Input Size: 8
  Output Size: 4
  Weight Size: Input Size x Output Size = 32
  Bias Size: Output Size = 4
I0
I1
I2
I3
I4
I5
I6
I7
O0
O1
O2
O3
∑
+ B0
x W0
x W1
x W2
x W3
x W4
x W5
x W6
x W7

## Slide 7: FC: Example
8x4 FC layer
  Input Size: 8
  Output Size: 4
  Weight Size: Input Size x Output Size = 32
  Bias Size: Output Size = 4
I0
I1
I2
I3
I4
I5
I6
I7
O0
O1
O2
O3
∑
+ B1
x W8
x W9
x W10
x W11
x W12
x W13
x W14
x W15

## Slide 8: FC: Example
8x4 FC layer
  Input Size: 8
  Output Size: 4
  Weight Size: Input Size x Output Size = 32
  Bias Size: Output Size = 4
I0
I1
I2
I3
I4
I5
I6
I7
O0
O1
O2
O3
∑
+ B2
x W16
x W17
x W18
x W19
x W20
x W21
x W22
x W23

## Slide 9: FC: Example
8x4 FC layer
  Input Size: 8
  Output Size: 4
  Weight Size: Input Size x Output Size = 32
  Bias Size: Output Size = 4
I0
I1
I2
I3
I4
I5
I6
I7
O0
O1
O2
O3
∑
+ B3
x W24
x W25
x W26
x W27
x W28
x W29
x W30
x W31

## Slide 10: FC: Example
8x4 FC layer
I ∙ W + B = O
X
Inner product
+
=

## Slide 11
LAB Overview

## Slide 12: Background: Overall Structure of FC layer
FC_Controller
BRAM
(Xilinx IP)
MAC
module
MAC
module
MAC
module
FC_TOP

## Slide 13: Background: Overall Structure of FC layer
FC_Controller
BRAM
(Xilinx IP)
MAC
module
MAC
module
MAC
module
FC_TOP
BRAM(Block RAM)
SRAM which FPGA can provide (different from LUT, FF) Usually used when we need to store lots of data
Can use BRAM by exploiting IP(Intellectual property)

## Slide 14: Background: Overall Structure of FC layer
FC_Controller
BRAM
(Xilinx IP)
MAC
module
MAC
module
MAC
module
FC_TOP
MAC(Multiplier Accumulator)
Module which performs addition & multiplication,
Takes A,B,C as an input and outputs A*B+C

## Slide 15: Background: Structure of FC layer
FC_Top
DRAM
BRAM
(Xilinx IP)
MAC
MAC
MAC
FC_Layer
FC_control_path
Control Path
Data Path
Host (PC)

## Slide 16: Background: Structure of FC layer
FC_Top
DRAM
BRAM
(Xilinx IP)
MAC
module
MAC
module
MAC
module
FC_Layer
FC_control_path
Host
Test
Bench
BRAM
(Xilinx IP)
MAC
module
MAC
module
MAC
module
FC_Controller
Output
Input, Weight, Bias

## Slide 17
Overview of the FC controller

## Slide 18: High Level Diagram of FC Controller (fc_controller.v)
r_valid
in_data
out_data
t_valid
clk
rstn
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight
MAC
clk
rstn
en
data_a
data_b
data_c
mout
done
partial_sum
result_acc
result_q
out_data
t_valid
FC Controller

## Slide 19: FSM of FC Controller (fc_controller.v)

## Slide 20: Flow of FC Controller (fc_controller.v)
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
data_set_done
Idle
r_valid
Accumulate
Idle
data_ready
Bias
Add
element_counter >= INPUT_SIZE-1
Data
Send
t_valid
out_counter < OUTPUT_SIZE
out_counter >= OUTPUT_SIZE
BRAM FSM
FC Calculation FSM

## Slide 21: Flow of FC Controller (fc_controller.v)
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
data_set_done
Idle
r_valid
clk
rstn
r_valid
in_data
out_data
t_valid
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight

## Slide 22: Flow of FC Controller (fc_controller.v)
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
data_set_done
Idle
r_valid
clk
rstn
r_valid
in_data
out_data
t_valid
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight

## Slide 23: Flow of FC Controller (fc_controller.v)
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
data_set_done
Idle
r_valid
clk
rstn
r_valid
in_data
out_data
t_valid
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight
input_set_done

## Slide 24: Flow of FC Controller (fc_controller.v)
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
bram_oreg_set_done
Idle
r_valid
clk
rstn
r_valid
in_data
out_data
t_valid
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight
bias_set_done

## Slide 25: Flow of FC Controller (fc_controller.v)
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
bram_oreg_set_done
Idle
r_valid
clk
rstn
r_valid
in_data
out_data
t_valid
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight
weight_set_done
bram_oreg_set_done

## Slide 26: Flow of FC Controller (fc_controller.v)
Accumulate
Idle
bram_oreg_set_done
Bias
Add
element_counter >= INPUT_SIZE-1
Data
Send
t_valid
out_counter < OUTPUT_SIZE
out_counter >= OUTPUT_SIZE
input_data
weight_buff
bias
weight
MAC
clk
rstn
en
data_a
data_b
data_c
mout
done
partial_sum
out_data
t_valid

## Slide 27: Flow of FC Controller (fc_controller.v)
Accumulate
Idle
bram_oreg_set_done
Bias
Add
element_counter >= INPUT_SIZE-1
Data
Send
t_valid
out_counter < OUTPUT_SIZE
out_counter >= OUTPUT_SIZE
input_data
weight_buff
bias
weight
MAC
clk
rstn
en
data_a
data_b
data_c
mout
done
partial_sum
out_data
t_valid
bram_oreg_set_done
copy

## Slide 28: Flow of FC Controller (fc_controller.v)
Accumulate
Idle
bram_oreg_set_done
Bias
Add
element_counter >= INPUT_SIZE-1
Data
Send
t_valid
out_counter < OUTPUT_SIZE
out_counter >= OUTPUT_SIZE
input_data
weight_buff
bias
weight
MAC
clk
rstn
en
data_a
data_b
data_c
mout
done
partial_sum
out_data
t_valid
mac_ireg_set_done

## Slide 29: Flow of FC Controller (fc_controller.v)
Accumulate
Idle
bram_oreg_set_done
Bias
Add
element_counter >= INPUT_SIZE-1
Data
Send
t_valid
out_counter < OUTPUT_SIZE
out_counter >= OUTPUT_SIZE
input_data
weight_buff
bias
weight
MAC
clk
rstn
en
data_a
data_b
data_c
mout
done
partial_sum
out_data
t_valid
2s’1

## Slide 30: Flow of FC Controller (fc_controller.v)
Accumulate
Idle
bram_oreg_set_done
Bias
Add
element_counter >= INPUT_SIZE-1
Data
Send
t_valid
out_counter < OUTPUT_SIZE
out_counter >= OUTPUT_SIZE
input_data
weight_buff
bias
weight
MAC
clk
rstn
en
data_a
data_b
data_c
mout
done
partial_sum
out_data
t_valid

## Slide 31: Flow of FC Controller (fc_controller.v)
BRAM Operation
  (1) If 'r_valid' == 1, change 'state’ to STATE_DATA_RECEIVE because the tb is ready to send data (STATE_IDLE)
  (2) Write 'input’, ‘weight’, 'bias’ into the BRAM (STATE_DATA_RECEIVE)
  (3) Read input data from the BRAM, then store it in the 'input_data’ (STATE_INPUT_SET)
  (4) Read bias data from BRAM, then store it in ‘bias’ (STATE_BIAS_SET)
  (5) Read weight data from the BRAM then store it in register ‘weight_buff’. Since the weight is too large to be stored in a register at once, store only 8-bytes of the weight (which corresponds to a single output). After storing 8-bytes of the weight, set ‘bram_oreg_set_done’ to 1. If ‘mac_ireg_set_done’ == 1, then prepare for the next weight since it means 'weight_buff’ ‘s value is moved to 'weight’
  Repeat (5) for 4 times!

## Slide 32: Flow of FC Controller (fc_controller.v)
FC Calculation Operation
  (1) If ‘bram_oreg_set_done' == 1, move value of 'weight_buff’ to ‘weight’ and set ‘mac_ireg_set_done’ to 1 (STATE_IDLE)
  (2) Use a single MAC. Get two 1-byte data from ‘input_data’, 'weight’ each and put them into data_a, data_b of the MAC unit. After computation, put the result into data_c and put the next input and weights into data_a, data_b (Reuse MAC). Repeat step (2) 8 times to get a single output (STATE_ACCUMULATE)
  (3) Add the summation result from step (2)and bias by using the MAC unit (STATE_BIAS_ADD)
  (4) Repeat step (2)~(3) 4 times, then convert the final output to 8-bits (quantization). Set ‘t_valid’ to 1 to push ‘out_data’ to testbench

## Slide 33
Part 1: BRAM Implementation

## Slide 34: Part 1: BRAM
Objectives
  Generate BRAM module with Block RAM generator IP (which Vivado provides)

## Slide 35: How to add BRAM IP (1)
(1) Click the IP Catalog tab
(2) Search “Block Memory Generator” in the search bar
(3) Double click the Block Memory Generator tab

## Slide 36: How to add BRAM IP (2)
(4) Enter “sram_32x16” in the Component Name section

## Slide 37: How to add BRAM IP (3)
(5) Configure all options as follows, then click OK button
Memory Size section
  Write Width: 32
  Read Width: 32
  Write Depth: 16
  Read Depth: 16
Operating Mode
  Select No Change
Primitives Output Register
  Deselect

## Slide 38: How to add BRAM IP (4)
(6) Click the Generate button
# of CPU cores that Vivado will use for generate process
This process may take some time,
So please wait with patience!

## Slide 39: How to add BRAM IP (5)
(7) After generation, you can see that BRAM IP is added in Sources

## Slide 40
Lets start coding in Verilog!

## Slide 41: Parts
Part2 : Reading data from BRAM and writing it into a register
Part3 : Mac operations
Part4 : Quantization
If you are comfortable with Verilog, you can just skip the instructions and implement the FC controller in the “hard” folder
Otherwise, follow the step by step tutorial in the “easy” folder
  Don’t worry if you didn’t finish the previous step!
  You can proceed by copying the files completed until the previous step

## Slide 42
Part2 : Reading data from BRAM

## Slide 43: BRAM Background
BRAM ports description
BRAM의 Input / Output |  |  |  |  | 
Input |  |  | Output |  | 
Name | Size | Description | Name | Size | Description
clk | 1-bit | Clock |  |  | 
bram_en | 1-bit | Enable |  |  | 
write_en | 1-bit | Write Enable (1: Write, 0: Read) | dout | 32-bit | Data from BRAM
addr | 4-bit | Address |  |  | 
din | 32-bit | Data written into BRAM |  |  | 

## Slide 44: BRAM Background
BRAM write
  Enable the BRAM when “r_valid” is 1
    r_valid: signal notifying that the testbench is sending data
    Change the flags with the data to be written
      bram_en : 1
      we : 1
      addr : address for storing the data
      din : data to be written
      Set “b_write_done” 1
      Writing data into BRAM is done in 1 cycle
  Terminate the execution at the next cycle
    bram_en <= 0
    we <= 0
    addr <= 4’b1111
      We use the last address for the default value (dump value)
BRAM_WRITE code

## Slide 45: BRAM Background
BRAM read
  Enable the BRAM when entering the state
    bram_en <= 1
    we <= 0
    addr <= {address for reading data}
  BRAM sends the data 1 cycle after receiving the changed flags
    The data is available from the “dout” port
  Terminate the execution after setting the registers with the data
    bram_en <= 0
    addr <= 4’b1111

## Slide 46: BRAM Background
Point 1
  Set both “bram_en” and “we” high
  In the next cycle, “din” is written at the “addr”
Point 2
  Set “bram_en” high
  One cycle later after setting the flag, the target data is received from “addr”
Point 1
Point 2

## Slide 47: We will implement the ”Bias Set” state
Data
Receive
Input
Set
b_write_done
Bias
Set
Weight
Set
input_set_done
bias_set_done
weight_counter > OUTPUT_SIZE
bram_oreg_set_done
Idle
r_valid
clk
rstn
r_valid
in_data
out_data
t_valid
dina
clka
addra
ena
wea
douta
BRAM
input_data
weight_buff
bias
weight
bias_set_done

## Slide 48: We will implement the ”Bias Set” state
TODO : Line 249 in fc_controller.v
Read the bias values from the BRAM and save them in the “bias” register
Hint : the code is very similar to STATE_INPUT_SET

## Slide 49
Part3 : Mac operations

## Slide 50: MAC
Reuse the MAC unit to compute the output
I7
W7
I0
W0
0
I1
W1
B0
1
O0
9 times

## Slide 51: Set the correct MAC input values
TODO : Implement lines 460 ~ 462 so that the input to the MAC unit is set properly
The MAC unit performs operations in the STATE_ACCUMULATE and STATE_BIAS_ADD state

## Slide 52
Part4 : Quantization

## Slide 53: Quantization Rule (1)
Layer structure
  Input : 8-bit 2’s fixed point input, weight, bias
  Output: 8-bits 2’s fixed point
Don’t quantize the intermediate result!
  To minimize data loss
Quantize the final calculated (MAC) result to 8-bit 2’s fixed point
  But you should consider overflow condition when you perform quantization (next slide)
To do so, set OUT_BITWIDTH of MAC large to ensure no loss
  ex) For this lab, up to two 8-bits fixed points are multiplied nine times to produce results
  result (15bit) + result(15bit) + ... + result(15bit)
  Excluding signed bit, then result can have up to 18 bits (7 + 7 + ┌ log2(9) ┐)
  So the result can be expressed with 19 bits, including signed bit
  We recommend setting C_BITWIDTH to 18 bits, OUT_BITWIDTH to 19 bits

## Slide 54: Quantization Rule (2)
Convert 19-bit 2’s fixed point (result) to 8-bit 2’s fixed point
  result[18]: Signed bit
  result[17:13]: Bits used for checking overflow
  result[12:6]: Real data after conversion
  result[5:0]: Dumped data
  Example
    1_11111_0100101_010010  1_0100101
    0_00000_1110111_000001  0_1110111
    Positive overflow (=0111_1111), Negative overflow(=1000_0000)
Pros and Cons of quantization
  Pros: Can reduce data size / Fast communication is enabled
  Cons: Accuracy is reduced

## Slide 55: Check for overflow & quantize the output values
TODO : Implement lines 496, 475 so that the output value is quantized properly
Convert “result_accurate” to “result_quantized” by using the provided quantization rules

## Slide 56
Final output

## Slide 57: Simulation Outputs
Result
  Check out the tcl console result
Correct case
Incorrect case
(Failed on consecutive test)
 Please check initialization of values!

## Slide 58
Wires & Regs

## Slide 59: Wires & Regs related to Buffer
Name | Explanation
input_data | A register containing partial input data from BRAM, where the value is fed into the MAC unit
weight | A register containing partial weights from BRAM, where the value is fed into the MAC unit
weight_buff | A register containing partial weights from BRAM, where the value is fed into the weight register
bias | A register containing partial bias data from BRAM, where the value is fed into the MAC unit

## Slide 60: Wires & Regs related to BRAM
Name | Explanation
r_valid | A flag indicating that the test bench is sending data to BRAM
b_state | A 3-bit register used for keeping track of the BRAM state
addr | Address to access BRAM
din | Data which will be written to BRAM
dout | Data read from BRAM
bram_en | A flag indicating whether r/w to BRAM is enabled
write_en | A flag indicating the BRAM operation mode (1 : write, 0 : read)
delay | A counter for keeping track of the delay of BRAM reads since it takes 2 cycles
b_write_done | A flag indicating that the data sent from the testbench are all written into the BRAM
input_set_done | A flag indicating that a subset of input values in BRAM are written into the input_data register
weight_set_done | A flag indicating that a subset of weight values in BRAM are written into the write_buffer register
bias_set_done | A flag indicating that a subset of bias values in BRAM are written into the bias register
bram_counter | A counter for keeping track of the number of BRAM reads
bram_oreg_set_done | A flag indicating that the input_data, weight and bias registers are all read from the BRAM and written to registers
weight_counter | A counter for keeping track of how many weight vectors corresponding to an output element were read

## Slide 61: Wires & Regs related to FC (fc_controller.v)
Name | Explanation
c_state | A 3 bit register for keeping track of the MAC unit state
mac_en | A flag indicating whether to enable the MAC unit and perform computation
data_a | A register containing a value (a in a * b + c) which will be used by the MAC unit
data_b | A register containing a value (b in a * b + c) which will be used by the MAC unit
data_c | A register containing a value (c in a * b + c) which will be used by the MAC unit
mac_done | A flag indicating that the MAC unit has finished its’ operation
element_counter | A counter keeping track of the number of accumulations that the MAC unit has performed (8 in this expermient)
partial_sum | An intermediate value when calculating the FC layer (It stores the output of the MAC unit and is fed into the MAC unit)
result_accurate | The output of the MAC unit
result_quantized | A register containing the 8-bit quantized value of result_accurate
mac_ireg_set_done | A flag to indicate that the data in the weight_buff has been successfully moved to the weight register, and new values can be loaded into the weight_buff (for parallelization)
out_counter | A counter for keeping track of which output element is currently being calculated
t_valid | A flag indicating that the fc_controller is ready to send the fc computation result back to the testbench